## Slide 1
5G: an IP Engineer Perspective
Federico Cossu
Consulting Engineer | IP/Optical Networks
federico.cossu@nokia.com

## Slide 2
From analog voice to high speed Internet
A Brief History of Mobile Networks
1980
1990
2000
2010
2020
1G
Analog Voice
Nokia Cityman
Nokia 3210
No Data
2G
Digital Voice
100s of kbps
3G
Mobile Data
10s of Mbps
iPhone 3G
4G
Mobile Broadband
100s of Mbps
5G
iPhone X
?

## Slide 3
ITU-R IMT-2020 performance goals
What Is 5G?
Peak Data Rate (Gbps)
User Experienced Data Rate (Mbps)
Spectrum Efficiency
Mobility (Km/h)
Latency (ms)
Connection Density (devices/km2)
Energy Efficiency
Area Traffic Capacity (Mbps/m2)
20
100
3x
500
1
106
4G
5G
100x
10
1
0.1
10x
1x
105
10
350
1x
10
1
Peak Data Rate
User Experienced Data Rate
Spectrum Efficiency
Mobility
Latency
Connection Density
Energy Efficiency
Area Traffic Capacity
High
Importance
Medium
Low
Massive Machine
Type Communications
Enhanced Mobile
Broadband
Ultra Reliable And Low
Latency Communications
Source: ITU-R M.2038.0

## Slide 4
Main nodes and functions
Recap: 4G/LTE Evolved Packet Core
MME: Mobility Management Entity
SGW: Serving Gateway
PGW: PDN Gateway
eNB: eNodeB (Radio)
SGW
MME
Internet
eNB
PGW
IP Core
S11
S5
S1-MME
S1-U
Mobility and Session Management
Interface to Subscriber Database
Mobility Anchor Point
Session Management
Packet Forwarding
IP Anchor Point
Session Management
Packet Forwarding
Interface to Policy, Charging, etc.
SGi

## Slide 5
Combined control and user plane over IP
Recap: 4G/LTE Architecture and Traffic Flows
SGW
eNB
MME
Internet
eNB
PGW
IP Core
Backhaul
IP
UDP
GTP-U
IP
IP
SCTP
S1-AP
User Plane (S1-U)
Control Plane (S1-MME)
X2
IP
MME: Mobility Management Entity
SGW: Serving Gateway
PGW: PDN Gateway
eNB: eNodeB (Radio)
GPS/
SyncE/
1588v2/
NTP
IP
UDP
GTP-U
IP
S11
IP
UDP
GTP-C
S5

## Slide 6
Main nodes and functions
5G Architecture: Native Control and User Plane Separation
gNB
UPF
UPF
Internet
Internet
SMF
AMF
N3
N2
N4
N4
N6
N9
N6
SBA Bus
NAMF
NSMF
Distributed User Plane
Centralized User Plane
AMF: Access and Mobility Management Function
SMF: Session Management Function
UPF: User Plane Function
SBA: Service Based Architecture
gNB: gNodeB (Radio)
User Plane
Control Plane
Session Management
Mobility Management
Packet Forwarding

## Slide 7
Same backhaul protocol stack with REST control plane
5G Architecture and Traffic Flows
UPF
gNB
AMF
Internet
gNB
IP Core
Backhaul
IP
UDP
GTP-U
IP
IP
SCTP
NG-AP
User Plane (N3)
Control Plane (N2)
Xn
IP
GPS/
1588v2
N6
SBA Bus
NAMF
NSMF
N4
IP
TCP
HTTP/2
REST/JSON
IP
UDP
PFCP
SMF
AMF: Access and Mobility Management Function
SMF: Session Management Function
UPF: User Plane Function
SBA: Service Based Architecture
gNB: gNodeB (Radio)

## Slide 8
Requires a service-aware backhaul network
5G Network Slicing for “Network as a Service”
gNB
AMF
N3
N2
UPF
DN
SMF
N4
N6
SBA Bus
NAMF
UPF
DN
SMF
N4
N6
UPF
DN
SMF
N4
N6
UPF
DN
SMF
N4
N6
NSSF
NNSSF
TE-enabled
Backhaul
NSSF: Network Slice Selection Function

## Slide 9
CRAN architecture introduces CPRI for the Fronthaul network
RAN Densification: Searching for Better Radio Coordination
EPC: Evolved Packet Core
RRH: Remote Radio Head
BBU: Baseband Unit
Centralized RAN
S/PGW
RRH
RRH
RRH
BBU Pool
Backhaul
Fronthaul
eNBs
Time Division Multiplexing
IQ
Data
Vendor
Specific
Ethernet
HDLC
L1 In-band
Protocol
User Plane
Control &
Management
Sync
CPRI: Common Public Radio Interface
Requires Dedicated
Fiber (xWDM)
Ultra low delay variation (16ns)
P2P constant bitrate stream

## Slide 10
Targeting a 10X increase in throughput
5G New Radio Main Technology Innovations
1GHz
6GHz
24GHz
mmWave
New Spectrum Options
Larger Radio Channels
Up to 400MHz
Massive MIMO

## Slide 11
CPRI bandwidth explosion with massive MIMO
Current CRAN Architecture Unfit for 5G Deployments
1Gbps
10Gbps
100Gbps
1000Gbps
1Tx
20MHz
4Tx
20MHz
64Tx
20MHz
64Tx
100MHz
1
4
64
320
*Approximate values

## Slide 12
RAN protocol stack split options
Addressing the Fronthaul Bandwidth Challenges
PDCP
Option 7
RLC
MAC
PHY
RF
RRC
IP
Option 6
Option 5
Option 4
Option 3
Option 2
Option 1
Layer 1
Layer 2
Max.
Latency
CPRI
Option 8
PDCP
Option 7
RLC
MAC
PHY
RF
RRC
IP
Option 6
Option 5
Option 4
Option 3
Option 2
Option 1
High
Layer
Low
Layer
Option 8
Required
Bandwidth

## Slide 13
Cloud RAN with packet-based transport
5G NR Introduces a New RAN Architecture
EPC/5GC
RU
RU
RU
DU
Backhaul
Fronthaul
CU
Midhaul
gNB
F1
Xn
NG/S1
NG/S1
CU: Centralized Unit
DU: Distributed Unit
RU: Radio Unit
DU
DU
F1
F1
RU
RU
RU
DU
CU
gNB
F1
DU
DU
F1
F1
Low Layer Split
(Option 7-2a)
High Layer Split
(Option 2)

## Slide 14
Designed for packet-based networks
eCPRI: Fronthaul Transport over Ethernet
User
Data
Real-Time
Control
Other
eCPRI
Services
Synchronization
Connection
OAM
C&M
eCPRI Protocol Header
eCPRI Services
UDP (Optional)
SyncE
PTP
SSH,
SNMP, etc
ICMP
UDP, TCP,
etc.
IP
IP (Optional)
Ethernet (Etype:AEFE)
VLAN+PCP
MACSec
Ethernet
OAM

## Slide 15
Savings of 10x compared to CPRI
eCPRI Fronthaul Bandwidth Estimations
236
Gbps
236
Gbps
Down
Up
Option 7-2
(Uplink)
User/
Up
Control/
Up
20
Gbps
<10
Gbps
User/
Down
Control/
Down
Basic Assumptions:
  100MHz
  8x4 MIMO (w/ 2 streams per uplink layer)
  64 Antennas
  TTI: 1ms
  Modulation: 256QAM
  *3Gbps downlink from MAC layer
  *1.5Gbps uplink to MAC layer
CPRI
Option 7-2
(Downlink)
eCPRI
20
Gbps
<10
Gbps
Drives 25GE interfaces

## Slide 16
Direct implication on inter-node distances
IEEE1914.1 & eCPRI Recommended One-Way Latency
Fiber Latency=5𝜇s/km
RU
Backhaul
Fronthaul
DU
5G Core
Midhaul
CU
UPF
>10ms
(50𝜇s for URLLC)
1ms
100𝜇s
>2000km
(10km for URLLC)
200km
20km

## Slide 17
QoS for mixing Fronthaul with other traffic flows
IEEE 802.1CM – Time Sensitive Networks
4
3
1
Fronthaul
2
Other
4
3
1
2
Egress port:
Profile A: Strict Priority
Fronthaul: High Priority
Other: Low Priority
1
3
4
2
Egress port:
1
Frame
Preemption
Profile B: Frame Preemption (<10GE only)
Fronthaul: Express Traffic
Other: Preemptable Traffic
Supported Today
Requires MAC Change
(mated boxes on a link)
Ingress traffic

## Slide 18
Radio and IP/Transport planning must be done together
No One-Size Fits-All Solution
5G Core
RU
Backhaul
(>10ms)
Fronthaul
(100us)
Midhaul
(1ms)
DU
CU
5G Core
DU+RU
CU
5G Core
RU
CU+DU
5G Core
CU+DU+RU
Backhaul
(>10ms)
Backhaul
(>10ms)
Midhaul
(1ms)
Fronthaul
(100us)
Backhaul
(>10ms)
DATA CENTER/NFVI

## Slide 19: 5G slicing
Introducing slicing concept and 5G use-cases

## Slide 20
Residential
1
Fixed Wireless Access (FWA) [5G TTH]
Improved reachability, coverage and capacity
Enable MNOs to enter new markets, offer new services
Verticals
2
5G hotspots
Allow VR/AR content delivery at large public venues
Allow eMBB
Industrial applications; smart cities
Enable build-outs of private and public infrastructures
New vertical segments and business models
3
UAVs (drones); autonomous vehicles
Enable new types of services for expanded market opportunities; fleet management, traffic control etc.
5
Healthcare; infotainment
Telemedicine, bandwidth/ latency sensitive communications
Mass delivery of video-driven services
4
5G deployment areas and use cases are mostly driven by Verticals…

## Slide 21
One size does not “fit all“
Why 5G network slicing?
10kbps - Meter/sensor (IoT)
100kbps & 2ms - Gaming
10Mbps - video streaming
1Mbps - Web browsing
Pre-5G era
10 kbps for IoT
100 kbps & 2ms for gaming
10 Mbps for video streaming
1 Mbps for Web browsing
Network Slice
virtual network with certain SLA (latency, throughput etc.)
5G era

## Slide 22: End to end network slicing
Infotainment
HD maps
Automated driving
Video surveillance
Public Safety
Automated driving
Edge
Core
PS Video surveillance
Multi-source artificial intelligence
BMW infotainment
BMW HD maps
Public & private clouds
Tenants
End to end network slices
RAN slices
Transport slices
Core slices
Hard vs. Soft Slicing
ITNOG5

## Slide 23
On the road to 5G use cases
What we can do with all of this?
1 Video surveillance & analytics
2 Machine remote control
3 Assisted & autonomous vehicles
4 Cloud robotics & process automation
5 eHealth
6 Fixed Wireless Access
7 Immersive experience
8 Smart Stadium

## Slide 24
UPF
UPF
Internet
Rapid broadband coverage in greenfield areas
Fixed-wireless Access with LTE and 5G (NSA)
Fixed-wireless access
LTE
5G NR
GTP (S1-U)
GTPv2 (S11)
MME
BNG +
S/PGW
PCRF/
AAA
Sx
EPC-NAS
S1-MME
Gx
Fixed Wireless Gateway
S/PGW
CPF
BNG
CPF
Multi-access
User Plane
:
UPF
eNB
gNB
Far Edge
(CO)
Aggregated
Edge
Data
Center
UE
Fixed-wireless Access Gateway
Combined SGW/PGW/BNG function
Features limited/relevant to residential broadband deployment (fixed-wireless APN).
Enable rapid broadband coverage in greenfield through fixed-wireless.
5G trials for fixed-wireless (FTTH alternative).
Software upgrade on existing BNGs.
DHCP (including DHCPv6-PD) over GTP-u supported.
CPF
ITNOG5

## Slide 25
UPF
Gi
UPF
Data
network
Expanding broadband capacity and reach
Hybrid access - Bonding Fixed & Mobile Access
Hybrid access
Fixed-wireless
access
LTE
5G NR
GTP (S1-U)
GTPv2 (S11)
MME
BNG +
S/PGW
PCRF/
AAA
Sx
EPC-NAS
S1-MME
Gx
Hybrid Access Gateway
Hybrid Access Services
Bonding fixed + wireless access
- Network bonding (GTP)
- Session bonding (MP TCP)
Augment fixed access capacity
Offload LTE network
Resilience (Access redundancy)
Single IP address, sign-on
Rapid service activation
S/PGW
CPF
BNG
CPF
Multi-access
User Plane
:
UPF
Wireline access
xDSL
FTTx
HFC
eNB
gNB
Far Edge
(CO)
Aggregated
Edge
Data
Center
CPE
CPF
ITNOG5

## Slide 26
Thank You!