## Slide 1: RPKI: a practical guide
Flavio Luciani - NAMEX
Marco Paesani – Fiber Telecom
Massimiliano Stucchi – Ripe NCC
ITNOG5 - Bologna, 10th May 2019
securitas securitate mutua paciscenda est

## Slide 2: Internet routing
What we call “The Internet” is actually an interconnection of autonomous, independent networks which use BGP to exchange routing information
  BGPv4, 1994
  No built-in security in BGP protocol
AS 1
193.x.x.x
AS 2
195.x.x.x
IRR
AS1=193.x.x.x
AS2=195.x.x.x
query
query

## Slide 3: Incidents are common
A route leak or a route hijacks is defined as the illegitimate advertisement of an IP space
2018 routing security review
  12.6k incidents
  4.4% of all ASNs affected
  3k ASNs victims of at least one incident
  1.3k ASNs caused at least one incident
source: https://www.bgpstream.com/

## Slide 4: Limitations of the Routing Registry
Many exist, most widely used
  Ripe database
  RADB
  ....
Not every RIR has a IRR
No verification of holdership over resources
The IRR system is far from complete (obsolete data)

## Slide 5: Accuracy
RIPE IRR
RADB IRR

## Slide 6: What is RPKI (1)
Resource Public Key Infrastructure is a PKI framework designed to secure the Internet Infrastructure
  Helps to secure Internet routing by validating routes
The 5 RIRs hold a self-signed root certificate for all the resources they have in the registry
The root certificate is used to sign a certificate that lists your resources
The certificate hierarchy follows the same structure as the Internet Number Resource allocation
All certificates are published in publicly accessible repositories

## Slide 7: What is RPKI (2)
RPKI uses X.509 certificates with extensions for IP addresses and AS identifiers described in RFC 3779
In RPKI, certificates do not include identity information, they only purpose is to transfer the right to use Internet Number Resources
LIRs are allowed to obtain a resource certificate listing the Internet number resources they hold, including their own public key (https://portal.ripe.net/rpki-enduser)
LIRs can then create cryptographic attestations about the prefixes they would announce (https://my.ripe.net/#/rpki)
These attestations are called Route Origin Authorizations (ROAs), signed prefixes

## Slide 8: Route Origin Authorisations
Digitally signed objects that associate one AS to one or more blocks of IP addresses
ROAs state which AS is authorised to originate certain IP prefixes
ROAs are published in the same repositors as certificates
LIRs can create a ROA for each of their resources (IP address ranges)
Multiple ROAs can be created for an IP range
Origin ASN
MAX LENGTH
Prefix
the network for which you are creating a ROA
The ASN supposed to be originating the BGP announcement
The maximum prefix length accepted for this ROA

## Slide 9: Hosted RPKI solution
RIRs decided to provide a hosted RPKI solution to lower the barrier into the technology
Hide all the crypto complexity
Just focus on creating and publishing ROAs
Easy-of-use in terms on maintenance and flexibility
Users login into the RIR member portal and request a resource certificate

## Slide 10: Route Origin Validation
A dedicated software (validator) downloads a local copy of all signed objects from the RIRs
The result is a list of all valid combinations of ASNs and prefixes, the “validated cache”
Validated ROA contents are called “Validated ROA Payload” (VRPs)
Routers query the validator software (rtr protocol) to check for prefixes validity
RIPE NCC
ARIN
AFRINIC
LACNIC
APNIC
RIRs
VALIDATOR
RPKI RTR PROTOCOL
ROUTER
rsync/rrdp

## Slide 11: The decision process
When you receive a BGP announcement from your peers, you can compare this to the validated cache
There are three possible outcomes:
  Unknown: there is no covering ROA for this prefix
  Valid: A ROA matching the prefix and ASN in found
  Invalid: There is a ROA but it does not match the origin ASN and/or maxLength
Based on this and on BGP announcements, you can instruct your router to make some decisions:
  modify LP
  Filter the announement
  ....
ROA
ROA
ROA
ROA
BGP ANNOUNCEMENTS
BETTER ROUTING DECISION

## Slide 12: RPKI Validator Software
Routinator
  https://www.nlnetlabs.nl/projects/rpki/routinator/)
Ripe NCC Validator
  https://www.ripe.net/manage-ips-and-asns/resource-management/certification/tools-and-resources
OctoRPKI
  https://github.com/cloudflare/cfrpki#octorpki
rcynic
  https://github.com/dragonresearch/rpki.net

## Slide 13: Statistics
RIPE NCC: 7632
APNIC: 1885
LACNIC: 1184
ARIN: 577
AFRINIC: 132
NUMBER OF CERTIFICATES
NUMBER OF ROAs
RIPE NCC: 9375
APNIC: 2732
LACNIC: 2241
ARIN: 4655
AFRINIC: 215

## Slide 14: ROAs for Italian Resources
Valid ROAs: 742
Invalid ROAs: 29
Invalid ROAs wrong ASN: 5
Invalid ROAs wrong length: 24
Unknown ROAs: 3906

## Slide 16: Implementazione
Support for Origin Validation and RPKI-RTR (draft form) first added in Junos 12.2R1 (September 2012).
  And all subsequent releases
Currently:
  RFC 6810 (“The Resource Public Key Infrastructure (RPKI) to Router Protocol”),
  RFC 6811 (“Prefix Origin Validation”)
  draft-ietf-sidr-origin-validation-signaling-08.
Supported on all products (physical and virtual) running Junos.
Implementazione validazione RPKI "up & running”
  Network: Fiber Telecom AS 196753
  Routers: MX960 con JUNOS ver. 18.1R3-S3.8
  RPKI cache: RIPE RPKI Validator

## Slide 17: Local RPKI Cache
Configuriamo la Local RPKI Cache (dinamica)
  La configurazione del local potrà essere IPv4 e/o IPv6
  Massimo due sessioni di validazione

## Slide 18: Static entry
Configuriamo una rete (statica)
Definiamo le reti RPKI localmente sul router
Problema realmente accaduto a marzo 2019

## Slide 19: Validazione delle reti
La validazione della rete viene definita come una normale policy di Junos verificando il contenuto del validation-database
La configurazione della policy funzionerà normalmente:
  impostando il valore della variabile (validation-state variable)
  impostando un altro stato (origin-validation-signaling community)
  accettando, rifiutando o modificando la LocalPref
  ............

## Slide 20: Configurazione della policy RPKI
La validazione della rete viene definita come una normale policy di Junos verificando il contenuto del validation-database

## Slide 21: Configurazione della policy di import e community
Le comunity sono indicate su RFC 8097
Valore in decimale 17152:X

## Slide 22: Management and troubleshooting
Show commands
  show route
  show validation statistics
  show validation database
  show validation replication
  show validation group
  show validation session
Request validation policy
  Re-run validation, optionally against only specified routes

## Slide 23: Show route

## Slide 24: Validation states
Gli stati di validazione interni al router (RFC 6811)
  valid
  invalid
  unknown
C'è anche un altro stato “validation was not run against this at all”
  unverified
Unverified è differente da unknown
La parte di rete internal BGP sarà unverified (best practice)

## Slide 25: Show validation statistics

## Slide 26: Show validation database & session

## Slide 27: Conclusioni
adottare RPKI-validation è una valida soluzione per problemi DDoS
adottare anche tutte le altre best practice per filtrare le rotte BGP
consiglio validazione OOB su network privato
informare e aggiornare i colleghi del NOC e documentare l’implementazione
configurare sempre rpf-check in modalità loose sulle interfacce esterne
non installare la default (IPv4 0.0.0.0/0 e/o IPv6 ::/0)
configurare quanto prima sul tuo backbone RPKI

## Slide 28: Q&A?
THANKS!
Flavio Luciani – f.luciani@namex.it
Marco Paesani – m.paesani@fibertelecom.it
Massimiliano Stucchi – max@stucchi.ch